A very minimal guide o use GRAPE-4

J. Makino Nov 16 1998

You need to use the following three functions:

--- attach GRAPE-4 hardware to the current process

      call h3open

      h3open_(); (in C)


---  calculate force

      call accel_by_harp3_separate_noopen(ni, xi,
     $     nj,xj,mj,a,p,eps2)

      accel_by_harp3_separate_noopen_(ni,xi, nj,xj,mj,a,p,eps2);
      (in C)


      integer NI
      int * ni;
           : number of i-particles (which receive the force)
           THIS COULD BE AN ARBITRARY NUMBER, not limited by the
           physical number of chips on the board. This routine will
           take care of the differ3ence
      real*8 XI(3,NI)
      double xi[][3];
           : locations of i-particles
      integer NJ : number of j-particles (which exert the force)
           This should not exceed (128k/3*NBOARDS), the phyisical
           memory size of the GRAPE-4 system (if you use treecode,
           it's pretty unlikely that you have more than 42k
           j-particles... 
      real*8 XJ(3,NJ): locations of j-particles
      real*8 MJ(NJ)  : mass of j-particles
      real*8 A(3,NJ): calculated accelerations
      real*8 P(NJ)  : calculated potential energies (includes
                      self-interaction)
      real*8 eps2   : softening length squared

NOTE:  when you use this function, MAKE THE SIZE OF the arrays for XI,
A and P LARGER THAN what is actually used, by at least 96 (the
physical number of pipelines). This routine might write some garbage
in locations after NI.

--- release GRAPE-4
     call h3close

     h3close_();
     (in C)

sample file minimal.f :

      program demo_2body
      integer ndim, nmax, ni, nj
      parameter(ndim=3,nmax=1024)
      real*8 x(ndim,nmax),a(ndim,nmax),p(nmax),m(nmax),eps2
      integer i,k
      ni = 2
      nj = 2
      do i = 1,ni
         do k = 1, ndim
            x(k,i) = 0
         end do
         m(i) =1
      end do
      x(1,1) = 1
      x(1,2) = -1
      eps2 = 0.01
      
      call h3open
      call accel_by_harp3_separate_noopen(ni, x, nj,x,m,a,p,eps2)
      do i = 1, ni
         write(6,600)'X ',(x(k,i),k=1,3), ' M ', m(i)
         write(6,600)'A ',(a(k,i),k=1,3), ' P ', p(i)
 600     format(A, 3g17.8, A, g17.8)
      end do
      call h3close
      end

sample file minimal.c

/*
 * minimal.c
 * minimal source to demonstrate the use of GRAPE-4
 */

#define NDIM 3
#define NMAX 1024


double  x[NMAX][NDIM];
double  a[NMAX][NDIM];
double  p[NMAX];
double  m[NMAX];

main()
{
    int ni, nj, i, k;
    double eps2;
    ni = nj = 2;
    for(i=0;i<ni;i++){
	for(k=0;k<NDIM;k++){
	    x[i][k] = 0.0;
	}
	m[i] = 1.0;
    }
    x[0][0] = 1;
    x[1][0] = -1;
    eps2 = 0.01;
    h3open_();
    accel_by_harp3_separate_noopen_(&ni, x, &nj,x,m,a,p,&eps2);
    for(i=0;i<ni;i++){
        printf("X %17.8g %17.8g %17.8g M %17.8g\n",
	       x[i][0], x[i][1], x[i][2], m[i]);
        printf("A %17.8g %17.8g %17.8g P %17.8g\n",
	       a[i][0], a[i][1], a[i][2], p[i]);
    }
    h3close_();
}

sample makefile:

minimal.h3: minimal.f
	f77 -o minimal.h3 -u minimal.f  -L/usr2/makino/src/harp3board -lharp3  -lrt -lm 
minimal.g4a: minimal.f
	f77 -o minimal.g4a -u minimal.f  -L/usr2/makino/src/pci-harp3/export/library -lg4a -lrt -lm 
cminimal.h3: minimal.c
	cc -o cminimal.h3 minimal.c  -L/usr2/makino/src/harp3board -lharp3  -lrt -lm 


H3: for old interface (can run on oppenheimer and pineau)
G4A: for new PCI interface (can run on steinberger, latour, muscat)

sample output:

<pineau:/usr2/makino/src/harp3board>make -f Makefile.minimal ; minimal.h3 
f77 -o minimal.h3 -u minimal.f  -L/usr2/makino/src/harp3board -lharp3  -lrt -lm 
(set_number_of_boards_from_environment) : nb=1
(set_firstcluster_from_environment) : nb=-1
(setup_offsets) nchips = 62
X     1.0000000       0.00000000E+00   0.00000000E+00 M     1.0000000    
A   -0.24906534       0.00000000E+00   0.00000000E+00 P    -10.499375    
X    -1.0000000       0.00000000E+00   0.00000000E+00 M     1.0000000    
A    0.24906534       0.00000000E+00   0.00000000E+00 P    -10.499375    
<pineau:/usr2/makino/src/harp3board>make -f Makefile.minimal cminimal.h3 
cc -o cminimal.h3 minimal.c  -L/usr2/makino/src/harp3board -lharp3  -lrt -lm 
<pineau:/usr2/makino/src/harp3board>cminimal.h3
(set_number_of_boards_from_environment) : nb=1
(set_firstcluster_from_environment) : nb=-1
(setup_offsets) nchips = 62
X                 1                 0                 0 M                 1
A       -0.24906534                 0                 0 P        -10.499375
X                -1                 0                 0 M                 1
A        0.24906534                 0                 0 P        -10.499375
<pineau:/usr2/makino/src/harp3board>